## Slide 1: Adders, Digital to Analog Conversion
PHY 201 (Blum)
<number>
Ch. 8 in Digital Principles (Tokheim)

## Slide 2: Most significant/least significant
PHY 201 (Blum)
<number>
Recall that in a number such as 1234, the numbers are weighted according to their position: 11000 + 2100 + 310 + 41
Because the 1 in 1234 is weighted by the largest power of ten, it is called the most significant digit.
Because the 4 in 1234 is weighted by the smallest power of ten, it is called the least significant digit.

## Slide 3: Adding Binary Numbers
PHY 201 (Blum)
<number>
Same as decimal; if the sum of two digits in a given position exceeds the base (10 for decimal, 2 for binary) then there is a carry into the next higher position
 | 1 | 
 | 3 | 9
+ | 3 | 5
 | 7 | 4
Carry

## Slide 4: Some terminology
PHY 201 (Blum)
<number>
Adding is a particular way of combining (acting on) two numbers to get another number.
A general term for an action is an operation.
The numbers that are being acted upon are known as operands.
Since addition requires two operands, it is known as a binary operation.
  We do not have to be adding binary numbers for the addition operation to be binary.

## Slide 5: Adding Binary Numbers
PHY 201 (Blum)
<number>
 | 1 |  |  | 1 | 1 | 1 | 
 | 0 | 1 | 0 | 0 | 1 | 1 | 1
+ | 0 | 1 | 0 | 0 | 0 | 1 | 1
 | 1 | 0 | 0 | 1 | 0 | 1 | 0

## Slide 6: Adding Binary Numbers
PHY 201 (Blum)
<number>
0 | 1 | 0 | 0 | 1 | 1 | 1 | 0
 | 0 | 1 | 0 | 0 | 1 | 1 | 1
+ | 0 | 1 | 0 | 0 | 0 | 1 | 1
 | 1 | 0 | 0 | 1 | 0 | 1 | 0
Carry in
Carry out

## Slide 7: Addition Logic
PHY 201 (Blum)
<number>
Addition can always be done two digits at a time (but does not have to be done that way).
  If there is a carry from a lower digit, the two digits can be added and then the carry can be added to that result.
There are two outputs:
  The sum (often denoted with an S or a ) is the number that has the same position (weighting) in the answer as the two digits being added.
  A carry (often denoted with a Co) is the number to be included in the next higher positional order.
    The carry may be zero, i.e. no carry.
    The o subscript indicates that the carry is an output of the operation.

## Slide 8: Half Adder Truth Table
PHY 201 (Blum)
<number>
INPUT |  | OUTPUT | 
A | B | Sum A XOR B | Carry-out A AND B
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
“Half adder” implies no carry-in input is included.

## Slide 9: Half-adder gate version
PHY 201 (Blum)
<number>

## Slide 10: Half to Full
PHY 201 (Blum)
<number>
The previous circuit is called a half adder, it adds two binary digits.
However, there may have been a carry from summing the lower digits, so the half adder does not represent all that can occur in adding the binary digits of a given positions.
For that we go to the so-called full adder.

## Slide 11: Full Adder Truth Table
PHY 201 (Blum)
<number>
INPUT |  |  | OUTPUT | 
Carry-in | A | B | Sum | Carry-out
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 12: Full-adder logic gates
PHY 201 (Blum)
<number>
Can be made with two half adders and an OR gate.

## Slide 13: Building up
PHY 201 (Blum)
<number>
In the preceding circuit we simply used two half adders and an OR gate to construct a full adder.
Let us examine the Karnaugh map for a full adder to see if any simplifications are possible.

## Slide 14: Sum output (Karnaugh)
PHY 201 (Blum)
<number>
A | B\ Cin | 0 | 1
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 1 | 0 | 1
1 | 0 | 1 | 0

## Slide 15: Checkerboard Pattern
PHY 201 (Blum)
<number>
In the previous truth table, there were no groups of 1’s containing more than a single 1.
Hence there are no simplifications.
For convenience, we represent it by a single logic gate (the excluded OR).

## Slide 16: 2-Input Excluded OR
PHY 201 (Blum)
<number>

## Slide 17: Not a genuine simplification
PHY 201 (Blum)
<number>
While replacing two NOTs, two ANDs and an OR by one XOR would appear to be a simplification, it is not a real simplification.
  Similarly the 3-input XOR replacing three NOTs, four ANDs and an 4-input OR is not a real simplification.
A real measure of simplification is whether it reduces the total number of transistors; it does not.
Another real measure is whether it reduces the number of “layers” of transistors (how many transistors the current must pass through); again it does not.

## Slide 18: Carry-out output (Karnaugh)
PHY 201 (Blum)
<number>
A | B\ Cin | 0 | 1
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 1 | 1 | 1
1 | 0 | 0 | 1
Hey, isn’t that the majority rules logic?

## Slide 19: Karnaugh version of adding
PHY 201 (Blum)
<number>

## Slide 20: Advantage
PHY 201 (Blum)
<number>
The circuit on the right has the advantage in terms of layers. There are six layers of gates (XOR counts as three) in the first circuit and only three in the second.

## Slide 21: Adding more than one positional digit
PHY 201 (Blum)
<number>
In the way most of us learned to add, we need to know the result of summing the lower digits since they might contribute a carry to the next higher digit.
In other words, the carry out of the lower digit addition becomes the carry in of the next higher digit addition.

## Slide 22: Ripple adder
PHY 201 (Blum)
<number>
A circuit built upon this logic is known as a ripple adder

## Slide 23: A problem
PHY 201 (Blum)
<number>
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 
 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1
+ | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 24: The problem with ripple adders
PHY 201 (Blum)
<number>
Your lowest-bit answer must be stable for you to have the correct input for the next highest digit.
Then that answer must be stable for you to have the correct input for the next highest digit.
Etc., etc., etc.,

## Slide 25: The problem with ripple adders
PHY 201 (Blum)
<number>
Each stabilization requires time.
The more digits one is adding, the more time is required.
Eventually the total time would exceed the period of one’s clock.
The problem with ripple adders is that they do not scale!

## Slide 26: Scaling
PHY 201 (Blum)
<number>
To scale something is to change its size.
If changing a system’s size does not introduce difficulty, the system is said to be scalable to simple to scale.
  Can we change the word size?
  Can we add records to a database?
  Can we add more computers to a network?

## Slide 27: Scalable addition
PHY 201 (Blum)
<number>
Addition requires only combinatorial logic, the output depends solely on the input and not on any previous state of the system (i.e. no memory is required)
  It is not “sequential”
Combinatorial truth tables can always be realized in three stages (NOTing, ANDing and ORing)
So a scalable addition is possible.

## Slide 28: The price
PHY 201 (Blum)
<number>
The scalable addition is more complicated circuitry.
The number of inputs of some of the logic gates (known as the fan-in) becomes large, and the gate must be able to handle that.
Similarly the output of a logic gate might be fed in as the input of many other gates (this is known as fan-out).

## Slide 29: Subtracting
PHY 201 (Blum)
<number>
One could examine from scratch the subtraction logic (borrows, etc.)
But it’s easier to note that A-B is equal to A+(-B).
So subtraction is negation followed by addition.
We’re adding a layer to the logic (the operation of negation then followed by the operation of addition. versus one operation: subtraction) but it is not layer after layer, so this subtraction will scale if the addition scales.

## Slide 30: Two’s Complement
PHY 201 (Blum)
<number>
One could represent negative numbers in various ways, the way that is convenient for integer addition and subtraction is the two’s complement representation.
  Other representations require one to break the problem into cases:
    Adding positive to positive
    Adding positive to negative
    Adding negative to positive
    Adding negative to negative

## Slide 31: Two’s Complement
PHY 201 (Blum)
<number>
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
+ | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0
Take inverse
Add 1 to the lowest bit
Unless stated otherwise, signed integers in this class will use the two’s complement representation.

## Slide 32: Digital to Analog
PHY 201 (Blum)
<number>
Here we show one way to convert from a binary digital signal (highs and lows only) to a quasi-analog signal (a signal with more intermediate values).
The device performing this task is known as a digital-to-analog converter or DAC.

## Slide 33: Inside versus Outside
PHY 201 (Blum)
<number>
Inside a computer the information is in digital form, but the outside world is analog.
To send sound to a speaker, to send an image to a monitor, etc. require converting digital information to analog information.

## Slide 34: Intermediate values means fractions
PHY 201 (Blum)
<number>
In the end we want not just high or low but intermediate or fractions values.
Thus we will use our notion of binary fractions as the digital input.
  To obtain a voltage that is half of the high voltage, we will use the binary number corresponding to ½.
  To obtain a voltage that is one quarter of the high voltage, we will use the binary number corresponding to ¼ .
  Etc.

## Slide 35: Fractions
PHY 201 (Blum)
<number>
Similar to what we’re used to with decimal numbers
3.14159 = | 3 · 100 + 1 · 10-1 + 4 · 10-2 + 1 · 10-3 + 5 · 10-4 + 9 · 10-5
11.001001 = | 1 · 21 + 1 · 20 + 0 · 2-1 + 0 · 2-2 + 1 · 2-3 + 0 · 2-4 + 0 · 2-5 + 1 · 2-6
(11.001001  | 3.140625)

## Slide 36: The other piece of the puzzle
PHY 201 (Blum)
<number>
Recall that the highs and lows we are talking about are high and low voltages.
Voltage is the energy that a charge has.
When flowing through a circuit a charge must use up all of its voltage (energy) before returning home.
The charges divides its energy among the tasks at hand (resistances). Thus at some intermediate point in the circuit, the charge has used up some fraction of it energy and still has the rest to use up.

## Slide 37: Resistors in Series
PHY 201 (Blum)
<number>
Resistors are in series if a charge that passes through the first has no choice but to pass through the second on its path around the circuit.
Still need to pass through one third of the resistance so need one third of the voltage.

## Slide 38: Resistors in Parallel
PHY 201 (Blum)
<number>
Resistors are in parallel if a charge can move through one or the other on its path around the circuit.
A combination of resistors in parallel has a smaller resistance than either constituent resistor.

## Slide 39: Voltage Divider
PHY 201 (Blum)
<number>
If two voltages are in series, part of the voltage is dropped across one resistor the rest across the second.
One can use this technique to reduce the voltage for devices that requires smaller voltages.

## Slide 40: Voltage Divider
PHY 201 (Blum)
<number>

## Slide 41: Voltage Divider
PHY 201 (Blum)
<number>

## Slide 42: D-to-A
PHY 201 (Blum)
<number>
The idea of the voltage divider can be extended to make a simple digital-to-analog converter.
The digital inputs can be thought of as binary decimals.
.101 would correspond to: 1/2 + 1/8 = 5/8

## Slide 43: Digital to Analog (00)
PHY 201 (Blum)
<number>
Nothing connected to high end of battery.
B is low
A is low

## Slide 44: Digital to Analog (10)
PHY 201 (Blum)
<number>
See next slide for rearranged circuit that’s easier to analyze.
B is high
A is low

## Slide 45: (10) Think of as
PHY 201 (Blum)
<number>
Resistors in parallel add reciprocally.
1/Req = 1/R1 +1/R2
Req=0.5 kOhm

## Slide 46: Digital to Analog (01)
PHY 201 (Blum)
<number>
B is low
A is high

## Slide 47: (01) Think of as
PHY 201 (Blum)
<number>
Req = 0.333 kOhm

## Slide 48: Digital to Analog (11)
PHY 201 (Blum)
<number>
B is high
A is high

## Slide 49: (11) Think of as
PHY 201 (Blum)
<number>
Req=0.333 kOhm